## Slide 1: 19eee131: Basic Electrical and Electronics Engineering Unit-V Operational Amplifiers

## Slide 2: contents
Introduction
Ideal OP-AMP
Inverting Configuration
Non-inverting Configuration
Voltage follower
Difference amplifiers(Single Op-amp & two Op-amps)
Applications of OP-AMP: Addition and Subtraction

## Slide 3: introduction
An operational amplifier is a Amplifier which amplifies the signal and member of Linear integrated circuits.
It is a high gain, negative feedback amplifier.
It can perform mathematical operations such as addition, subtraction, integration and differentiation.
It is used in voltage regulators, oscillator circuits, pulse generators, comparators, Analog to Digital and Digital to Analog converters, analog computers etc.
It is popularly known as OP-AMP.
It can amplify both d.c and a.c input signals.

## Slide 4: Op-Amp Symbol
(+) or ‘b’ is non-inverting terminal
(-) or ‘a’ is inverting terminal
‘a’ and ‘b’ input terminals
‘c’ output terminals
Positive voltage input V2 is applied to terminal ‘b’ and negative voltage input V1 is applied to terminal ‘a’.
Output voltage V0 = A(Vid) = A (V2-V1)
where A is the open loop gain of the amplifier

## Slide 5: The Ideal Op-Amp (Inverting)
Output voltage V0 = A(Vid) = A (0-V1) = -AV1

## Slide 6: The Ideal Op-Amp (Non inverting)
Output voltage V0 = A(Vid) = A (V2 - 0) = AV2

## Slide 7: The Ideal Op-Amp: equivalent circuit
Equivalent circuit is helpful in analyzing the operating principle of OP-AMP and in observing effects of feedback.
Ri is the input resistance appearing between inverting and non-inverting terminals.
R0 is the output resistance which is Thevenin equivalent resistance looking back from output terminals of OP-AMP.
‘AVid’ is the equivalent Thevenin voltage source.

## Slide 8: The Ideal Op-Amp: characteristics
Ideal OP-AMP has following characteristics:
An infinite voltage gain. i.e. A =
An infinite bandwidth. i.e. any frequency signal ranging 0 to
Hz can be amplified without any distortion.
Infinite input resistance. i.e. Ri = . Hence, input current is zero and no loading effect. OP-AMP is a voltage controlled device.
Zero output resistance. i.e. R0 = 0. Hence, V0 is independent of the output resistance.
When input signal voltage is zero, the output signal will also be zero.
Common mode rejection ratio (CMRR)is infinite.
Infinite slew rate. i.e. change in output voltage occurs simultaneously with the input voltage changes.

## Slide 9: The Ideal Op-Amp: characteristics

## Slide 10: The Ideal Op-Amp: Transfer characteristics
Voltage transfer characteristic curve is drawn between input (Vid) and output (V0) voltages.
Saturation of output voltage takes place once the differential input voltage ‘Vid’ reaches a threshold voltage ‘Vth’.
The saturation voltage is approximately equal to supply voltage for all practical considerations.
Slope of the curve represents the gain ‘A’.

## Slide 11: The Inverting Configuration: Open Loop
Input signal is applied to inverting input terminal.
The non-inverting terminal is grounded. i.e. V2 = 0.
Output voltage V0 = AOL(Vid) = AOL (0-V1) = - AOLV1.
Where AOL is open loop voltage gain which is very high.
The negative sign indicates that output is 1800 out of phase with respect to input.
As AOL is very high and –Vsat< V0<Vsat,
Hence V0 oscillates between +Vsat and -Vsat.
Hence, very small input voltages drives the output to saturation level.
So, only the small signals of the order of micro volts can only be amplified accurately without distortion.
Signals of high amplitudes can be applied by using feedback in the OP-AMP.

## Slide 12: The Inverting Configuration: Closed Loop
Figure shows basic inverting amplifier with feedback resistance Rf . In this mode positive input terminal is grounded and the signal is applied to the negative terminal.
V1 may be a d.c. or a.c. voltage signal with in the bandwidth of amplifier.
Output signal is fed back to the inverting input terminal through feedback resistance Rf .
The feedback current is algebraically added point G.
The point G, although not connected to ground, but is held virtually at ground potential irrespective of V1 and V0.

## Slide 13: The Inverting Configuration: Closed Loop
At point G, i1= i2.
Output voltage
Closed loop gain
If Rf= R1 = 1, then A = -1, and the amplifier is called unity gain amplifier with 1800 phase inversion.

## Slide 14: Concept of virtual ground
We know V0 = A (V+- V-) = A (Vid)
Gain of the amplifier is of order of 2X105
Let us take the output voltage V0 = 10V
V0 =10 = 2X105(Vid)
Hence, Vid =
Vid = V+- V- = 0
V+ =Vi and V- = 0 as it is grounded.
Hence, Vi = 0 and point G acts as virtual ground.

## Slide 15: The Non-inverting Configuration: Open Loop
Input signal is applied to non-inverting input terminal.
The inverting terminal is grounded. i.e. V1= 0.
Output voltage V0 = AOL(Vid) = AOL(V2 –V1) = AOLV2.
Where AOL is open loop voltage gain which is very high.
The output is in phase with respect to input.
As AOL is very high and –Vsat< V0<Vsat,
Hence V0 oscillates between +Vsat and -Vsat.
Hence, very small input voltages drives the output to saturation level.
So, only the small signals of the order of micro volts can only be amplified accurately without distortion.
Signals of high amplitudes can be applied by using feedback in the OP-AMP.

## Slide 16: The Non-inverting Configuration: Closed Loop
Figure shows basic non-inverting amplifier with feedback resistance Rf . In this mode negative input terminal is grounded through R1and the signal is applied to the positive terminal.
Output signal is fed back to the inverting input terminal through feedback resistance Rf .
The potential of point G, Vi= V+= V2
The feedback current is algebraically added point G.
Voltage across R1 is equal to V2 and Rf is (V0 –V2).

## Slide 17: The Non-inverting Configuration: Closed Loop
At point G, i1= i2.
,
Output voltage
Closed loop gain
A is always positive and greater than one and acts as positive scaler.

## Slide 18: Voltage follower
In this circuit Rf = 1,
V0 = Vi = V2
Voltage gain Av = 1.
Output voltage is equal and in phase with the input and the OP-AMP circuit acts as a voltage follower.
It is also called as source follower, isolating amplifier and buffer amplifier.

## Slide 19: Adder or Summing amplifier:
In analog computers OP-AMP circuits are used as summing amplifier circuit.
Figure shows three input summing amplifier circuit.
In the circuit
If R1=R2=R3=Rand substituting Vi= 0 (Virtual ground)
If R= 3Rf , the same circuit can be used for averaging and

## Slide 20: Differential amplifiers: Open loop
A differential amplifier amplifies the difference between two voltages V1 and V2 applied at both input terminals.
Their amplified difference appears at the output terminal.
V0 = A(V2-V1)

## Slide 21: subtractor or difference amplifier with two op-amps

## Slide 22: Single Op-Amp Differential amplifier
It is a combination of inverting and non-inverting amplifiers.
To calculate output voltage super position theorem is applied.
Vout is equal to sum of the individual responses of Vin1 and Vin2.
i.e Vout = Vout1 + Vout2

## Slide 23: Differential amplifiers: Closed loop
Calculation of Vout1:
as Riis infinitely large, V1 acts as virtual ground and is equal to zero.
, but

## Slide 24: Differential amplifiers: Closed loop
Calculation of Vout2:
as Riis infinitely large, V1 V2 =
, and substituting V1=V2
If R2=R1 and R3 = Rf, then

## Slide 25: Differential amplifiers: Closed loop
Vout = Vout1 + Vout2
The differential voltage gain